## Slide 1: Attitude estimation with Extended Kalman Filter
Mirko Mazzoleni - corso di Identificazione dei modelli e analisi dei dati

## Slide 2: Outline
For errors, contribution, discussion, write at: mirko.mazzoleni@unibg.it

## Slide 3: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 4: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 5: Introduction
Scope of the laboratory
Use the Kalman Filter to perform attitude estimation of a smartphone, using inertial platform measurements:
    Gyroscope
    Accelerometer
    Magnetometer
LPT: Access SAMSUNG smartphone sensors with the combination: *#0*#
    Reference  Orientation Estimation using Smartphone Sensors – Linkoping university

## Slide 6: Introduction
Frames
We will use two coordinate systems: the world frame and the sensor frame
These coordinate systems are related via linear transformations
where is a point expressed in the sensor frame and is the same point expressed in the world frame
The relative rotation between the two frames is given by , the rotation matrix
Since we consider only rotation, the term is discarded
Reference  Robotica: modellistica, simulazione e controllo
Siciliano, Sciavicco, Villani, Oriolo

## Slide 7: Introduction
Frames
The focus of this lab is to estimate the rotation based on the sensor measurements available from a smartphone
By estimating we are able to obtain the object attitude in the fixed frame
The world frame is fixed
The sensor frame rotate
and express the point coordinates in the two frames

## Slide 8: Introduction
Frames
A rotation matrix has 3 meanings:
Gives the orientation of one set of coordinates wit respect to another
Represents a coordinates transformation that relates the coordinates of the same point in two different frames
Is the operator which rotates a vector in the same frame

## Slide 9: Introduction
Attitude representation
An object attitude can be expressed via rotation matrices (9 elements)
The 9 elements are not independent because of orthogonality constraints  3 idenpendent parameters (3 angles)
Euler angles
ZYZ representation (current frame)
RPY representation (fixed frame)
PROBLEM: Singularities
Different position in the same have the same representation

## Slide 10: Introduction
Quaternions
Non minimal representatio (4 parameters) but with no singularities
Represent a rotation of an angle around the axis ,
We have that and represents the same rotation. So the representation of a rotation must be chosen according to the specific application

## Slide 11: Introduction
Rotation matrix corresponding to a quaternion

## Slide 12: Introduction
Time derivative of a quaternion
Discretize the derivative

## Slide 13: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 14: Model
Simple model
The unknown states are the quaternion components. We want to estimate them in order to obtain the object attitude which we do not measure (4-d vector)
Input: gyroscope measurements (3-d vector)
Outputs: accelerometers and magnetometer measurements (6-d vector)

## Slide 15: Model
Model state space equations

## Slide 16: Model
Linearization – state space matrix

## Slide 17: Model
Linearization – input matrix

## Slide 18: Model
Linearization – Output matrix

## Slide 19: Outline
Introduction
Model
Preprocessing and implementation of EKF

## Slide 20: Introduction
Steps
Check sensors frames on the smarthpone
Acquire static measurement to compensate for biases in the sensors
Calibrate magnetometer
Implement the code